## Slide 1: Digital Logic Fundamentals
Dr. Hammad Afzal
Military College of Signals
National University of Sciences and Technology, Pakistan
Spring, 2011
hammad.afzal@mcs.edu.pk

## Slide 2: Chapter 1 – Digital Systems and Binary Numbers

## Slide 3: Previously Done
Analog versus Digital Systems
Digitization of Analog Signals
Binary Numbers and Number Systems
Number System Conversions
Representing Fractions

## Slide 4: Today’s Talk
Signed-Magnitude Representation
Signed-Compliment Representation

## Slide 5: Signed Binary Numbers
It is usual to represent the sign with a bit placed in the leftmost position of the binary number
Sign bit
Sign bit 0 positive
Sign bit 1 negative
The Most common notations are:
Signed-magnitude system.
Signed-complement system.

## Slide 6: Signed-Magnitude System
The way we perceive in common arithmetic.
+ for positive and – for negative numbers
In Computers, to represent a +ve and –ve numbers in Signed-Magnitude Form
1 at left most position for negative number
0 at left most position for positive number

## Slide 7: Signed Magnitude System
01001  + 9
11001  – 9
3-bit binary pattern
Bit Pattern | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
Signed-Magnitude Decimal Value | +0 | +1 | +2 | +3 | -0 | -1 | -2 | -3
Example 1
Example 2

## Slide 8: Signed-Magnitude System
Signed and Unsigned numbers have different interpretations
(Details in Book)
Example
Signed Binary | Decimal Equivalent
01001 | +9
11001 | -9
Un-Signed Binary | Decimal Equivalent
01001 | 9
11001 | 25

## Slide 9: Signed Complement System
In this system, a negative number is indicated by its complement.
The signed-complement system can use either the 1’s complement or the 2’s complement notations

## Slide 10: Complements
Conventional addition (using carry) is easily implemented in digital computers.
However; subtraction by borrowing is difficult and inefficient for digital computers
Much more efficient to implement subtraction using ADDITION of the COMPLEMENTS of numbers

## Slide 11: Complements
Subtraction by addition
  R’s Complement
    In Binary 2’s complement
    In Decimal 10’s complement
  (R-1) Complement
    In Binary 1’s complement
    In Decimal 9’s Complement

## Slide 12: Diminished Radix (r-1) Complement
Given a number N in base r having n digits, its r-1 complement is
Decimal: (10n -1 ) - N
  If n=6 then 106-1=1000000-1=999999
  9’s complement of 546700 is 999999-546700=453299
  In simple words subtract each digit from 9
(rn -1 )-N

## Slide 13
Diminished Radix (r-1) Complement
The 9’s complement of 546700 is 999999 - 546700= 453299
And the 9’s complement of 12389 is
99999- 12389 = 87610.
5
4
6
7
0
-
0
9
9
9
9
9
9
4
5
3
2
9
9
1
2
3
8
-
9
9
9
9
9
9
8
7
6
1
0
Find the 9’s complement of 546700 and 12389
9’s Complement

## Slide 14: Diminished Radix (r-1) Complement
Binary: (2n -1 )-N
  If n=4 then 24= (16)10= (10000)2
  24 – 1 = (15)10= (1111)2
  Note: 1-0=1 and 1-1 =0 (Bit Changes)
  In simple words just change the bits
1’s Complement

## Slide 15
Diminished Radix (r-1) Complement
The complement 1’s of
1011001 is 0100110
0
1
1
0
0
-
1
1
1
1
1
1
1
1
0
0
1
1
0
0
0
1
1
1
-
1
1
1
1
1
1
1
1
1
0
0
0
0
1
1
0
The 1’s complement of
0001111 is 1110000
0
1
1
1’s Complement

## Slide 16: Radix (r) Complement
Given a number N in base r having n digits, its r complement is
Simply add one to the radix-1 complement
  (rn –N) = [(rn -1 )-N] +1
(rn –N)

## Slide 17: Radix (r) Complement
Find the 10’s complement of 546700 and 12389
The 10’s complement of 546700 is 1000000 - 546700= 453300
and the 10’s complement of 12389 is
100000 - 12389 = 87611.
5
4
6
7
0
-
0
0
0
0
0
0
0
4
5
3
3
0
0
1
2
3
8
-
9
1
0
0
0
0
0
8
7
6
1
1
1
Notice that it is the same as 9’s complement + 1.
10’s Complement

## Slide 18: Radix (r) Complement
2’s Complement
The 2’s complement of
1011001 is 0100111
The 2’s complement of
0001111 is 1110001
0
1
1
0
0
-
1
0
0
0
0
0
0
1
0
0
1
1
1
0
0
1
1
1
-
1
1
1
0
0
0
1
1
0
0
0
1
1
0
0
0
0
0
0
0
1

## Slide 19: Fast Computation of 2’s Complement
Method 1:
The 2’s complement of binary number is obtained by adding 1 to the l’s complement value.
Example:
1’s complement of 101100 is 010011 (invert the 0’s and 1’s)
2’s complement of 101100 is 010011 + 1 = 010100

## Slide 20: Fast Computation of 2’s Complement
Method 2
The 2’s complement can be formed by leaving all least significant 0’s and the first 1 unchanged, and then replacing l’s by 0’s and 0’s by l’s in all other higher significant bits.
Example:
The 2’s complement of 1101100 is
0010100
Leave the two low-order 0’s and the first 1 unchanged, and then replacing 1’s by 0’s and 0’s by 1’s in the four most significant bits.

## Slide 21: Example
Assuming the representation of the number 9 in binary with 8-bits, we have the following cases:
Unsigned 9 or +9 has a the same representation in both signed-magnitude and signed-complement systems which is: 00001001
-9 has the signed-magnitude representation: 10001001
-9 has the signed-1’s complement representation: 11110110
-9 has the signed-2’s complement representation: 11110111

## Slide 22: Signed Complement System
The signed-complement conversion table of a 3-bit binary pattern is as follows:
Bit Pattern | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
Signed 1’s complement decimal value | +0 | +1 | +2 | +3 | -3 | -2 | -1 | -0
Signed 2’s complement decimal value | +0 | +1 | +2 | +3 | -4 | -3 | -2 | -1

## Slide 23: Signed Complement System
4-bit system
Positive values Negative values

## Slide 24: Subtraction with r-Complement
Subtract N from M : M – N
r’s complement of N = rn – N
Add M to ( rn – N ); Result = M + ( rn – N)
if M  N, simply ignore the carry
if M < N, take the r’s complement of sum and place negative sign in front of sum. The answer is negative.

## Slide 25
Perform the subtraction 72532 - 13250 = 59282.
M > N : Case 1 Discard carry
The 10’s complement of 13250 is 86750.
Therefore:
M = 72532
10’s complement of N =+86750
Sum= 159282
Discard end carry 105= - 100000
Answer = 59282
Example 1
Notes: 25

## Slide 26
Now consider an example with M <N.
The subtraction 13250 - 72532 produces negative 59282. Using the procedure with complements, we have
M = 13250
10’s complement of N = +27468
Sum = 40718
Take 10’s complement of Sum = 100000
-40718
The number is : 59282
Place negative sign in front of the number: -59282
Example 2
Notes: 26

## Slide 27: Complement of Fractions
We can extend the idea of complement on fractions.
Examples:
  Negate 0101.01 in 1s-complement Answer: 1010.10
  Negate 111000.101 in 1s-complement Answer: 000111.010
  Negate 0101.01 in 2s-complement Answer: 1010.11