## Slide 1: Computer Organization and Architecture (BESE-15a)
Lecture 13
Dr. Hammad Afzal
13th Dec, 2010

## Slide 2: Cache Memory Cache Design

## Slide 3: Cache Design
Size
Mapping Function
Replacement Algorithm
Write Policy
Block Size
Number of Caches

## Slide 4: Replacement Algorithms (1) Direct mapping
No choice
Each block only maps to one line
Replace that line

## Slide 5: Replacement Algorithms (2) Associative & Set Associative
Least Recently used (LRU)
  e.g. in 2 way set associative, which of the 2 block is lru? (USE bit)
First in first out (FIFO)
  replace block that has been in cache longest
Least frequently used (LFU)
  replace block which has had fewest hits
  Use of counter
Random

## Slide 6: Write Policy
Problems:
  More than one device may have access to memory. For example, an I/O module.
    If word is altered only in cache, corresponding memory word is invalid. Vice versa
  Multiple CPUs connected to a bus with each having an individual caches

## Slide 7: Write Policy: Write through
All writes go to main memory as well as cache
  Multiple CPUs can monitor main memory traffic to keep local (to CPU) cache up to date
Disadvantages
  Lots of memory traffic
  Slows down writes

## Slide 8: Write Policy: Write back
Updates initially made in cache only
  Update bit for cache slot is set when update occurs
  If block is to be replaced, write to main memory only if update bit is set
Disadvantages
  Other caches get out of sync
  Portion of memory are invalid.
  I/O must access main memory through cache

## Slide 9: Line Size
Retrieve not only desired word but a number of adjacent words as well
Increased block size will increase hit ratio at first
  the principle of locality
Hit ratio will decrease as block becomes even bigger
Larger blocks
  Reduce number of blocks that fit in cache
  Data overwritten shortly after being fetched
  Each additional word is less local so less likely to be needed
No definitive optimum value has been found
8 to 64 bytes seems reasonable
For HPC systems, 64- and 128-byte most common

## Slide 10: Multilevel Caches
High logic density enables caches on chip
  Faster than bus access
  Frees bus for other transfers
Common to use both on and off chip cache
  L1 on chip, L2 off chip in static RAM
  L2 access much faster than DRAM
  L2 may now be on chip
  Resulting in L3 cache

## Slide 11: Unified v Split Caches
One cache for data and instructions or two, one for data and one for instructions
Advantages of unified cache
  Higher hit rate
    Balances load of instruction and data fetch
    Only one cache to design & implement
Advantages of split cache
  Eliminates cache contention between instruction fetch/decode unit and execution unit
    Important in pipelining

## Slide 12: Cache Memory Design Parameters
Cache size(in bytes or words)
  .A larger cache can hold more of the program’s useful data but is more costly and likely to be slower.
Block or cache-line size(unit of data transfer between cache and main).
  With a larger cache line, more data is brought in cache with each miss. This can improve the hit rate but also may bring low-utility data in.
Placement policy.
  Determining where an incoming cache line is stored. More flexible policies imply higher hardware cost and may or maynot have performance benefits (due to more complex data location).
Replacement policy.
  Determining which of several existing cache blocks (into which a new cache line can be mapped) should be overwritten. Typical policies: choosing a random or the least recently used block.
Write policy.
  Determining if updates to cache words are immediately forwarded to main (write-through) or modified blocks are copied back to main if and when they must be replaced (write-backor copy-back).