## Slide 1: Computer Organization and Architecture
Dr. Hammad Afzal
27th Oct, 2010

## Slide 2: Lecture 9
Addressing Modes
Chapter 11 of William Stallings's Book:
Computer Organization and Architecture

## Slide 3: Addressing Modes
An architecture addressing modes are the set of syntaxes and methods that instructions use to specify a memory address
  For operands or results
  As a target address for a branch instruction
When a microprocessor accesses memory, to either read or write data, it must specify the memory address it needs to access
Several addressing modes to generate this address are known, a microprocessor instruction set architecture may contain some or all of those modes, deepening on its design

## Slide 4: Addressing Modes
Immediate
Direct
Indirect
Register
Register Indirect
Displacement (Indexed)
Stack
Notes: 2

## Slide 5: Immediate Addressing
Operand is part of instruction
Operand = address field
e.g. ADD 5
  Add 5 to contents of accumulator
  5 is operand
No memory reference to fetch data
Fast
Limited range
Notes: 3

## Slide 6: Immediate Addressing Diagram
Operand
Opcode
Instruction
Notes: 4

## Slide 7: Direct Addressing
Address field contains address of operand
Effective address (EA) = address field (A)
e.g. ADD A
  Add contents of cell A to accumulator
  Look in memory at address A for operand
Single memory reference to access data
No additional calculations to work out effective address
Limited address space
Notes: 5

## Slide 8: Direct mode
Instruction includes the A memory address
LDAC 5 – accesses memory location 5, reads the data (10) and stores the data in the microprocessor’s accumulator
This mode is usually used to load variables and operands into the CPU
Address A
Opcode
Instruction
Memory
Operand

## Slide 9: Indirect Addressing (1)
Memory cell pointed to by address field contains the address of (pointer to) the operand
EA = (A)
  Look in A, find address (A) and look there for operand
e.g. ADD (A)
  Add contents of cell pointed to by contents of A to accumulator
Notes: 7

## Slide 10: Indirect Addressing (2)
Large address space
2n where n = word length
May be nested, multilevel, cascaded
  e.g. EA = (((A)))
Multiple memory accesses to find operand
Hence slower
Notes: 8

## Slide 11: Indirect mode
Starts like the direct mode, but it makes an extra memory access. The address specified in the instruction is not the address of the operand, it is the address of a memory location that contains the address of the operand.
LDAC (5), first retrieves the content of memory location 5, say 10, and then CPU goes to location 10, reads the content (20) of that location and loads the data into the CPU (used for relocatable code and data by operating systems)
Address A
Opcode
Instruction
Memory
Pointer to operand
operand

## Slide 12: Register Addressing (1)
Operand is held in register named in address filed
EA = R
Limited number of registers
Very small address field needed
  Shorter instructions
  Faster instruction fetch
Notes: 10

## Slide 13: Register Addressing (2)
No memory access
Very fast execution
Very limited address space
Multiple registers helps performance
  Requires good assembly programming or compiler writing
c.f. Direct addressing
Notes: 11

## Slide 14: Register direct mode
It specifies a register instead a memory address
LDAC R – if register R contains a value 5, then the value 5 is copied into the CPU’s accumulator
No memory access
Very fast execution
Very limited address space
Register Address R
Opcode
Instruction
Registers
Operand

## Slide 15: Register Indirect Addressing
C.f. indirect addressing
EA = (R)
Operand is in memory cell pointed to by contents of register R
Large address space (2n)
One fewer memory access than indirect addressing
Notes: 13

## Slide 16: Register indirect mode
LDAC (R) – the register contains the address of the operand in the memory
Register R (selected by the operand), contains value 5 which represents the address of the operand in the memory (10)
One fewer memory access than indirect addressing
Register Address R
Opcode
Instruction
Memory
Operand
Registers
Pointer to
operand

## Slide 17: Implicit addressing mode
Doesn’t explicitly specify an operand
The instruction implicitly specifies the operand because always applies to a specific register
This is not used for load instructions
This mode is used also in CPUs that do use a stack to store data; they don’t specify an operand because it is implicit that the operand must come from the stack